## Slide 1: Augmenting System Tests with Component Tests for Reliability Assurance
Joint work with Jace Ritchie and
Mike Hamada

## Slide 2: Overview
The reliability of products is of great interest to both manufacturers and customers
Testing can be expensive!
Our approach can reduce testing costs by replacing some system tests with component tests

## Slide 3: Background
Definition of an assurance test
Test plans consist of the number of required tests (n) and the number of acceptable failures (c) to pass the test.
Can control for two possible errors
  Consumer’s risk
  Producer’s risk
Define acceptable and rejectable reliability levels

## Slide 4: Bayesian Assurance Testing
Straightforward to incorporate prior knowledge through priors
Condition on two possible outcomes
  Test is passed (TIP)
  Test is failed (TIF)
Posterior risks are defined in terms of posterior probabilities
  Acceptable posterior consumer’s risk (PCR) is defined to be:
  Acceptable posterior producer’s risk (PPR) is defined to be:

## Slide 5: Consumer’s and Producer’s Risks
Both customers and manufacturers want the product to work well
Consumers want the posterior probability that the reliability is no more than a specified rejectable reliability level (πrrl) given the assurance test is passed to be low
Producers want the posterior probability that the reliability is at least a specified acceptable reliability level (πarl) given the assurance test is failed to be low

## Slide 6: Defining a Test Plan
A test plan is composed of two elements:
  The total number of assurance tests applied to the system or component (n)
  The number of acceptable system failures (c)
When a product has high reliability:
  PCR tends to be low when c is low and n is high
  PPR tends to be low when c is high and n is low
An acceptable test plan has PCR and PPR lower than some thresholds (β and α, respectively)
  In some situations, the choice is made not to control PPR

## Slide 7: How to find a Bayesian assurance test
Hamada et al. (2008) provide a graphical algorithm
  Choose β, α, , and
  Start with n=1 and c=0
  Iterate until the test satisfies both the posterior consumer's risk and the posterior producer’s risk
  The resulting n and c define the test

## Slide 8: What is a system?
A group of component parts and/or subsystems
Can be arbitrarily large and complex
We assume independence of components, the probability of a system failure can be modeled using basic statistical methods
In this work we only consider one-shot systems with either pass or fail a test

## Slide 9: Series Systems
The system fails when a single component fails
Under independence assumptions, its reliability is easily calculated
PPR and PCR are hard to calculate for large systems
We calculate PCR and PPR via Monte Carlo integration

## Slide 10: Parallel Systems
The system fails when every single component fails
Under independence assumptions, its reliability is easily calculated
PPR and PCR are hard to calculate for large systems
We calculate PCR and PPR via Monte Carlo integration

## Slide 11: Previous Work
Hamada et al. (2008, 2014) consider consumer’s and producer’s risks based assurance tests
Hamada et al. (2008, 2014), Ten and Xie (1998), and Guo et al. (2010) use beta distributions as prior distributions, but only consider PCR
Smith et al. (2010) considers zero-failure component assurance tests as well as maximizing posterior reliability under cost restraints

## Slide 12: Proposed Method
Allow component tests to be used directly in assurance tests
Now an assurance test plan consists of an “n” and a “c” for the system and each component (including subsystems)
Finding an assurance test plan is no longer a trivial exercise
Could result in large savings
Strong assumptions could lead to problems

## Slide 13: Assumptions
The system must be represented as a reliability block diagram
Components fail independent of each other
Components should be testable and have prior probability of failure
The cost of each component and system tests are known

## Slide 14: Phantom Components
What happens when the series isn’t a perfect series? Or when the parallel assumption doesn’t work?
Graves et. al. (2010) proposed using one or more latent components to approximate a series or parallel system
We relax the by adding a “phantom” (or latent) component
  Can’t be tested
  Very dependent on its prior
We generally assume violations of the series, parallel, or independence assumptions result in a smaller πs

## Slide 15: Complex Systems
Guo et al. (2010) consider the system as depicted but assume independence and don’t test subsystems

## Slide 16: Complex Almost-Series and Almost-Parallel Systems
Modified version of Guo et al. (2010) system
Subsystems can be testable and provide useful information
A phantom component is added for the whole system and for each testable subsystem

## Slide 17: Comparing Different Tests
PPR
PCR
α
β

## Slide 18: Overview of Algorithm to Find Test Plan
Find an acceptable test plan using only system tests
Remove one system test
Add a test to all components and repeat until we achieve an acceptable test plan
Remove individual component tests (most expensive first) while still maintaining acceptable PCR and PPR
Check the test is cheaper than the current iteration
Repeat start at step 2 until an acceptable and cheaper test can’t be found

## Slide 19: Modified Algorithm for System Tests
Hamada et al. (2008) provide the base for our algorithm
We adjust it by saving the values of ns and cs at every iteration
Doing so creates a framework for augmenting the system tests more efficiently

## Slide 20: How to Augment System Tests

## Slide 21: Simulation Study
We consider the four basic systems
All numbered components have beta(8,4) priors. Phantom components have beta(11,1) priors
We used these test conditions: α = β = 0.05, πarl = 0.95, and πrrl = 0.90
System tests cost 4 units and component tests cost 1 unit

## Slide 22: Simulation Results

## Slide 23: Application Setup

## Slide 24: Application – Informative Priors no PPR
We compare our results with those from Hamada et. al. (2014) and don’t consider PPR (i.e., cs = 0)
Each component had a beta(a,1) prior
Set β = 0.05, πrrl = 0.95
They found a test with ns = 7 and cs = 0 (assuming independence) (test cost is 1400)
We started with a test with ns = 13 and cs = 0 (using phantom components) (test cost is 2600)
Using component test we get a test cost of 156 (cost reductions of 1244 and 2444 units respectively)

## Slide 25: Application – Reference Priors & PPR
Here, we consider PPR. A lower cost test is found by using Jeffrey’s priors for testable components than informative priors
We started with a test with ns = 108 and cs = 0, where β = 0.05, πrrl = 0.95, πarl = 0.96, α = 0.05 (test cost of 21600)
Using component tests we obtain a cost of 7902 (a cost reduction of 13698 units)

## Slide 26: Discussion
Replacing system tests with component tests is useful when controlling for PCR and PPR
Often, a cheaper test can be found that doesn’t fully rely on system tests
Applications can include testing reliability of cost inhibitive systems or systems that cannot be tested but whose components can
Future work could include finding a more optimized algorithm for augmenting system tests as well as considering systems whose reliability is not measured as pass/fail

## Slide 27: Bibliography
Graves, T. L., Anderson-Cook, C. M., and Hamada, M. S. (2010). Reliability models for almost-series and almost-parallel systems. Technometrics, 52(2):160–171.
Guo, H., Jin, T., and Mettas, A. (2010). Designing reliability demonstration tests for one-shot systems under zero component failures. IEEE Transactions on Reliability, 60(1):286–294.
Hamada, M. S., Wilson, A., Reese, C. S., and Martz, H. (2008). Bayesian Reliability. Springer.
Hamada, M. S., Wilson, A. G., Weaver, B. P., Griffiths, R. W., and Martz, H. F. (2014). Bayesian binomial assurance tests for system reliability using component data. Journal of Quality Technology, 46(1):24–32.
Smith, C., Kelly, D., and Dezfuli, H. (2010). Probability informed testing for reliability assurance through Bayesian hypothesis methods. Reliability Engineering & System Safety, 95(4):361–368.
Ten, L. M. and Xie, M. (1998). Bayes reliability demonstration test plan for series-systems with binomial subsystem data. In Annual Reliability and Maintainability Symposium. 1998 Proceedings. International Symposium on Product Quality and Integrity, pages 241–246. IEEE.

## Slide 28
Thank you!